## Slide 1
Preliminary Presentation on Project on
“SMART WHEELCHAIR FOR PARALYZED”
Presented by
24. JASIRA T P
34. NAYANA RAMESHAN
46. SHRAVAN SREEDEEP
48. SOORYA P
under the guidance of
Dr. C SREEKUMAR
DEPARTMENT OF ELECTRICAL & ELECTRONICS ENGINEERING
GOVT. COLLEGE OF ENGINEERING KANNUR- 670563
April 2022

## Slide 2: OVERVIEW
Introduction
Objectives
Literature Review
Wheelchair Design
  Calculation of Rolling Resistance
  Calculation of Power
Work done In This Semester
Work Plan
Conclusion
Reference

## Slide 3: INTRODUCTION
Paralyzed stroke patients are unable to normally communicate with their environment.
Part of their body that is under their control is their eyeballs.
Basic day to day operations are switching on basic devices like fan, bulb etc.
Smart Wheel Chair is the solution that we are proposing for these problems.

## Slide 4: OBJECTIVES
To track eye movement and control basic devices like bulb, fan etc.
To design and implement an autonomous electric wheelchair.
To control the electric wheel chair by tracking eye movements.

## Slide 5: LITERATURE REVIEW
[1] Yi-Chen Lee, Ching-Min Lee, “Real-Time Smart Home Surveillance System of Based on Raspberry Pi”, IEEE, 2020
Home surveillance system, using Raspberry Pi, various sensing modules, and small devices to achieve essential home safety and smart home requirements
Remote control and foundational voice control functions

## Slide 6: LITERATURE REVIEW
[2] Muhammad Azlan Alim, Samsul Setumin, Anis Diyana Rosli, Adi Izhar Che Ani, “Development of a Voice-controlled Intelligent Wheelchair System using Raspberry Pi”, IEEE, 2021
Voice controlled intelligent wheelchair with obstacle detection feature is developed
Dual-controller mode emphasizes limited control over their lower limb or both limbs

## Slide 7: LITERATURE REVIEW
[3]V.Usha Rani, Dr.J Sridevi, P. Mohan Sai, “Web Controlled Raspberry Pi Robot Surveillance”, IEEE Conference, 2021
Robot can perform efficiently when connected to internet through a Wi-Fi
Cannot function on mobile data as the system requires a stable IP address for the Raspberry-Pi

## Slide 8: WHEEL CHAIR DESIGN
During the movement of a wheelchair, there are some resistances that appear.
  Rolling resistance
  Aerodynamic resistance
  Inertial resistance

## Slide 9: Calculation of Rolling Resistance
When an unformulated wheel is wrapped in unformed ground or, respectively, a fully resilient wheel is wound on a fully developed ground, there is no resistance to the movement.
In reality both the ground and the wheel suffer from deformations.
Tr = N×a ------(1)
To balance this torque, it is necessary to develop a torque opposite to this.
This torque equals the product of the pulling force Fr and the dynamic radius of the wheel.

## Slide 10: Calculation of Rolling Resistance
Vertical force (Fz) which expresses the mass of a body in strength equals to:
Fz = m×g -----------(2)
where m is the body mass and g is the acceleration of gravity.
The rolling resistance Fr is described by the following formula:
Fr = Fz × μr ------------(3)
Where μr is the rolling resistance coefficient which is estimated for the wheelchairs with non- pneumatic wheels on concrete, with the value of
μr = 0.015.

## Slide 11: Calculation of Rolling Resistance
For the calculation of the wheelchair rolling resistance is taken into account the masses of :
  Wheelchair, m1 = 7kg
  User, m2 = 100kg
  Battery, m3 = 2×2.5kg = 5kg
  Motor, m4 = 2×2.35kg = 4.7kg
  Auxiliary weight, m5 = 200g
  Total weight, M= m1+m2+m3+m4+m5
  = 7+100+5+4.7+0.2 = 116.9kg ≈ 117kg

## Slide 12: Calculation of Rolling Resistance
Fz = M ×g ----------(4)
Fz = 117 × 9.81
Fz = 1147.77 N
M is the total mass in kilogram
Fr = Fz×μr ------------(5)
Fr = 1147.77 × 0.015
Fr = 17.2 N

## Slide 13: Calculation of Rolling Resistance
When climbing a vehicle due to road inclination, a resulting force from the weight of the vehicle appears as shown in Fig 1.
This force opposes the movement of the vehicle when it is on the hill.
Fig 1. Forces in road inclinations.

## Slide 14: Calculation of Rolling Resistance
The ascent resistance FB is calculated from the following formula:
FB=Fz× Sin α--------------(6)
Where Fz is vertical force in newtons and α is the angle of the road inclination.
Tilt of the road is the ratio of the height H to the distance L (Fig 1) and expresses the height to be developed at a distance of 100 km:
Ι = Η/L = tan α ≈ sin α------------(7)
To find the angle α, in order to calculate the ascent resistance, the right formula is the following:
Α=tan-1(i)

## Slide 15: Calculation of Rolling Resistance
Thus, for a pavement slope of 10o the vehicle has an ascent resistance equals to:
FB= 1147.77 × Sin10 = 199.31 N
Ftotal= Fr + FB = 17.2+ 199.31 = 216.51 N
Where Ftotal is the total traction force which is the sum of ascent resistance FB and the rolling resistance Fr
The torque needed on the wheel to overcome these resistors is calculated by the formula:
Ft = Mk × itot/rt => Mk = Ft × rt / itot
Where Mk is the torque on the wheel in Nm

## Slide 16: Calculation of Rolling Resistance
The rt the radius of the wheel and itot its gear transmission ratio from the motor to the wheel.
The motors have a diameter of 12inch (308mm) with a working voltage of 24V, 250Watt and a fixed gear transmission ratio of 23: 1.
The maximum torque that can be produced by the motor according to its operating diagram is 20Nm and is enough to overcome the climb and roll resistors.
Ft = Mk × itot / rt
Mk = Ft × rt / itot
= 22 × 0.154 / 23
= 1.5 Nm

## Slide 17: Calculation of Rolling Resistance
According to standard values maximum speed of motor is 220 rpm and the maximum speed that the wheelchair can develop is 12Km/h.
This is calculated by the following formula:
N = V × 60/2 × π × r
V = n × 2 × π × r / 60
= 216.51 × 2 × π × 0.154/60
V = 3.50 m/s
V = 12.6 Km/h
Where V is the maximum speed that wheelchair can achieve in Km/h, n is motors speed in rpm and r is wheelchair’s wheel radius in m.

## Slide 18: Calculation of Power
Work results when a force acts upon an object to cause a displacement (or a motion) or, in some instances, to hinder a motion.
Three variables are of importance in this definition
  Force
  Displacement
  The extent to which the force causes or hinders the displacement
Each of these three variables find their way into the equation for work.
W=F×χ
Where W is the work in Joules, F is force in N and χ is the displacement in meters

## Slide 19: Calculation of Power
Considering the above mathematical formulas and knowing the velocity it follows that:
P = Ft×Vt
Where P is the power in watts Ft is the traction force in N and Vt is the velocity in m/s.
Theoretically, the power given to the vehicle, when it moves at the maximum speed (3.54m/s) it can develop:
P = Ft×Vt
P= 17.2N × 3.50 m/s P= 60.2 Watt

## Slide 20: Calculation of Power
The needed energy to drive the vehicle for one hour is calculated by the formula:
E= P×t
E = 0.0602KWh
Where E is the energy in KWh, P is power in watt and t is the time in hours.
According to the formula below, the vehicle needs 2.50Ah to move one hour at maximum speed.

## Slide 21: Calculation of Power
E =×V/1000
=0.0602×1000/24
= 2.50Ah
Where E is the energy needed in Ah, Qx is the capacity of the battery in Ah and V is the voltage of the battery used in the experiment equal to 24V.

## Slide 22: WORK DONE IN THIS SEMESTER
(S8)

## Slide 23: STATUS OF PROJECT WORK
Acquired and tested components of wheelchair.
Fig 2. Components

## Slide 24: STATUS OF PROJECT WORK
Fig 3. 250W, 24V, 13.7A Motor
Fig 4. 4 Channel Relay(Peak 30V DC Supply)

## Slide 25: STATUS OF PROJECT WORK
Fig 5. 12V, 7.2Ah Battery
Fig 6. Battery Charger and Connector

## Slide 26: STATUS OF PROJECT WORK
Fig 7. Node MCU
Fig 8. Ultrasonic Sensors

## Slide 27: STATUS OF PROJECT WORK
Fig 9. Webcam

## Slide 28: ESTIMATION OF COMPONENTS
SL No. | Component Name | Quantity | Price
1 | 250W, 24V, 13.7A Motor | 2 | 4600
2 | 4 Channel Relay(Peak 30V DC Supply) | 1 | 240
3 | 12V, 7.2Ah Battery | 4 | 3000
4 | 15V,2.2A Battery Charger | 1 | 250
5 | Node MCU | 1 | 500
6 | Ultrasonic Sensors | 4 | 400
7 | DC Wire Socket | 1 | 10
8 | Raspberry Pi 4 | 1 | 5100
9 | Webcam | 1 | 1500
10 | Wheelchair | 1 | 7000
11 | BTS7960B Bridge Motor Driver | 1 | 800

## Slide 29: RASPBERRY PI 4 CONFIGURATION
Materials required:
  Raspberry Pi 4
  RJ45 LAN cable
  32GB SD card and adapter
Software required:
  Raspberry Pi OS
  VNC Viewer and VNC Server
  PuTTY Software

## Slide 30: RASPBERRY PI INTERFACE
Fig 10. Raspbian OS Desktop Interface

## Slide 31: EYE TRACKING PROGRAM
Tested eye tracking program on Raspberry Pi 4
Fig 11. Eye tracking program on Raspberry Pi 4

## Slide 32: EYE TRACKING PROGRAM
Setup for Eye tracking program
Fig 12. Experimental Setup

## Slide 33: WORK PLAN
Work | Oct 2021 | Nov 2021 | Dec 2021 | 1-2 weeks Jan 2022 | 3-5 weeks Jan 2022 | Feb 2022 | Mar 2022 | April 2022 | May 2022
Topic selection and preliminary works |  |  |  |  |  |  |  |  | 
Literature Survey |  |  |  |  |  |  |  |  | 
Program and train machine learning model for eye tracking. |  |  |  |  |  |  |  |  | 
Simulation of autonomous wheelchair. |  |  |  |  |  |  |  |  | 
Simulation of the circuit for home automation. |  |  |  |  |  |  |  |  | 

## Slide 34: WORK PLAN
Work | Oct 2021 | Nov 2021 | Dec 2021 | 1-2 weeks Jan 2022 | 3-5 weeks Jan 2022 | Feb 2022 | Mar 2022 | April 2022 | May 2022
Interface the eye tracker, home automation and wheelchair together. |  |  |  |  |  |  |  |  | 
Purchase and test components |  |  |  |  |  |  |  |  | 
Hardware implementation of eye tracking glasses. |  |  |  |  |  |  |  |  | 
Hardware implementation of autonomous wheel chair. |  |  |  |  |  |  |  |  | 
Test and solve real time issues. |  |  |  |  |  |  |  |  | 

## Slide 35: CONCLUSION
Literature review for the proposed model are done.
Raspberry Pi 4 is acquired and tested.
Eye tracking model is developed.
Simulation of autonomous wheel chair.
Components for the wheelchair are purchased and tested.
Raspberry Pi 4 is configured for our wheelchair.
Next phase is the assembling of eye controlled wheelchair.

## Slide 36: REFERENCE
[1] Yi-Chen Lee, Ching-Min Lee, “Real-Time Smart Home Surveillance System of Based on Raspberry Pi”, IEEE, 2020
[2] Muhammad Azlan Alim, Samsul Setumin, Anis Diyana Rosli, Adi Izhar Che Ani, “Development of a Voice-controlled Intelligent Wheelchair System using Raspberry Pi”, IEEE, 2021
[3] V. Usha Rani, Dr. J Sridevi, P. Mohan Sai, “Web Controlled Raspberry Pi Robot Surveillance”, IEEE Conference, 2021

## Slide 37: THANK YOU

## Slide 38: LITERATURE REVIEW
[1]Tan Kian Hou, Yagasena and Chelladurai, “Arduino based voice controlled wheelchair”, IEEE, 2019
Smart motorized voice controlled wheelchair.
Voice command controls the movements of the wheelchair.
Microcontroller used is Arduino Uno.

## Slide 39: LITERATURE REVIEW
[2]Ahmad F. Klaib, Nawaf . Alsrehin, Wasen Y. Melhem, Haneen Bashtawi, Aws A. Magableh, “Eye Tracking Algorithms, Techniques, Tools, and Applications with an Emphasis on Machine Learning and Internet of Things Technologies”, September 2020.
Machine learning and the Internet of Things are essential factors in the development of eye tracking applications.
This eye tracking techniques have more accurate detection results compared with traditional event-detection methods.

## Slide 40: LITERATURE REVIEW
[3] Mohammed Hayyan Al Sibai, Sulastri Abdhul Manap, “A Study on Smart
Wheelchair Systems”, Research Gate Dec 2015
Presented different smart technologies for wheelchairs.
The human - machine interface and the navigation methods and devices, were the two key areas of concentration.

## Slide 41: SCHEMATIC DIAGRAM
CAMERA MODULE
RASPBERRY PI 4
NODE MCU
×8
DC MOTOR DRIVER
LEFT MOTOR
RIGHT MOTOR
Fig 1. Block Diagram of Smart Wheelchair
RELAY CIRCUIT

## Slide 42: SMART WHEELCHAIR
The whole project is divided into 3 parts
Eye tracking module using Raspberry Pi 4
Home automation system using Node MCU
Wheel Chair

## Slide 43: SMART WHEELCHAIR
Eye tracking module using Raspberry Pi 4
  Camera Module is used to capture eye movements.
  The eye movement is tracked using the python eye tracking model using Raspberry Pi 4.
  The position of the pupil is transferred to Node MCU.

## Slide 44
Fig 2. Flow Chart of Eye Tracking Program

## Slide 45: SMART WHEELCHAIR
Fig 3. Detection of Pupil in Tracking Program

## Slide 46: SMART WHEELCHAIR
Wheel Chair
  Wheel chair is also controlled on the basics of the control signal received from Raspberry Pi 4.
  The wheel chair have low speed for safety.
  8 ultra sonic sensors are connected in 4 directions of the wheelchair for obstacle and pit detection.
  Incase an obstacle is identified the wheel chair stops and trajectory can be corrected.

## Slide 47: SMART WHEELCHAIR
Home automation system using Node MCU
  From the position received from Raspberry Pi 4, appropriate decision is taken by the Node MCU.
  Control by Node MCU include the switches of light and fan.

## Slide 48: SMART WHEELCHAIR
Fig 4. Home Automation System Using Node MCU and Bluetooth Module

## Slide 49: WORK DONE IN PREVIOUS SEMESTER
(S7)

## Slide 50: STATUS OF PROJECT WORK
Simulation of Smart Wheel Chair
Fig 5. Simulation Model of Smart Wheelchair

## Slide 51: STATUS OF PROJECT WORK
Simulation of Smart Wheel Chair
Fig 6. Simulation Model of Smart Wheelchair

## Slide 52: STATUS OF PROJECT WORK
Simulation of Smart Wheel Chair
Fig 7. Simulation Model of Smart Wheelchair

## Slide 53: STATUS OF PROJECT WORK
Simulation of Smart Wheel Chair
Fig 8. Simulation Model of Smart Wheelchair

## Slide 54: STATUS OF PROJECT WORK
Simulation of Smart Wheel Chair
Fig 9. Simulation Model of Smart Wheelchair

## Slide 55: STATUS OF PROJECT WORK
Simulation of Smart Wheel Chair
Fig 10. Simulation Model of Smart Wheelchair

## Slide 56: STATUS OF PROJECT WORK
Eye tracking program is developed and its results are shown below.
Fig 11.Straight
Fig 12. Closed

## Slide 57: STATUS OF PROJECT WORK
Eye tracking program is developed and its results are shown below.
Fig 13. Left
Fig 14. Right

## Slide 58: STATUS OF PROJECT WORK
Acquired and tested Raspberry Pi 4, 4GB model.
Fig 15. Raspberry Pi 4